## Slide 1
ENME601 Thermodynamics
Tutorial Session
Presenter : Dr. Jay Wang

## Slide 2: Tutorial Questions (Week 5) Q1-Q10 Guidelines

## Slide 3: Tutorial Question Q1
Q1) An air compressor compresses 6 L of air at 120 kPa and 20°C to 1000 kPa and 400°C. Determine the flow work, in kJ/kg, required by the compressor.
Required flow work = change in flow work
The energy to push the fluid into a control volume

## Slide 4: Tutorial Question Q2
Q2) Air enters the 1-m2 inlet of an aircraft engine at 100 kPa and 20°C with a velocity of 180 m/s. Determine the volume flow rate, in m3/s, at the engine’s inlet and the mass flow rate in kg/s, at the engine’s exit.
Under steady-flow conditions, the principle of conservation of mass indicates that the mass flow rate at the inlet equals the mass flow rate at the exit.

## Slide 5: Tutorial Question Q3
Q3) Refrigerant-134a enters the compressor of a refrigeration system as saturated vapor
at 0.14 MPa and leaves as superheated vapor at 0.8 MPa and 60°C at a rate of 0.06 kg/s.
Determine the rates of energy transfers by mass into and out of the compressor.
Assume the kinetic and potential energies to be negligible.
Identify the properties at the inlet & exit
Use Table A-12 and A13

## Slide 6: Tutorial Question Q4
Q4) Air enters a 16-cm-diameter pipe steadily at 200 kPa and 20°C with a velocity of 5 m/s. Air is heated as it flows, and it leaves the pipe at 180 kPa and 40°C. Determine (a) the volume flow rate of air at the inlet, (b) the mass flow rate of air, and (c) the velocity and volume flow rate at the exit.
since
Air is an ideal gas – Use table A-1 to find gas constant.
For any open system, the rate at which mass enters the system must be the same as the rate at which mass exits the system.

## Slide 7: Tutorial Question Q5
Q5) A spherical hot-air balloon is initially filled with air at 120 kPa and 20°C with an initial diameter of 5 m. Air enters this balloon at 120 kPa and 20°C with a velocity of 3 m/s through a 1-m-diameter opening. How many minutes will it take to inflate this balloon to a 17-m diameter when the pressure and temperature of the air in the balloon remain the same as the air entering the balloon.
Assuming that the flow rate of air into the balloon is steady (doesn't vary with time), the volume flow rate can be defined to be the change in volume divided by the change in time.
Find out the initial and final volume and calculate the volume flow rate.

## Slide 8: Tutorial Question Q6
Q6) A 2m3 rigid tank initially contains air whose density is 1.18 kg/m3. The tank is connected to a high-pressure supply line through a valve. The valve is opened, and air is allowed to enter the tank until the density in the tank rises to 5.30 kg/m3. Determine the mass of air that has entered the tank.
Conservation of mass

## Slide 9: Tutorial Question Q7
Q7) Air at 600 kPa and 500 K enters an adiabatic nozzle that has an inlet-to-exit area ratio of 2:1 with a velocity of 120 m/s and leaves with a velocity of 380 m/s. Determine (a) the exit temperature and (b) the exit pressure of the air.
Apply the steady-flow energy balance to find the exit temperature:
Use Table A-17 to find properties of air
Use ideal gas equation to determine the air densities at inlet and outlet
Then apply the conversation of mass for pressure calculation.

## Slide 10: Tutorial Question Q8
Q8) An adiabatic air compressor compresses 10 L/s of air at 120 kPa and 20°C to 1000 kPa and 300°C. Determine (a) the work required by the compressor, in kJ/kg, and (b) the power required to drive the air compressor, in kW.
Apply energy balance:
(steady-flow, and changes in kinetic and potential energies are negligible)
Work required by the compressor: win ​=h2​−h1 ​(Use table A-17)
Power required to drive the compressor:

## Slide 11: Tutorial Question Q9
Q9) Refrigerant-134a is throttled from the saturated liquid state at 700 kPa to a pressure of 160 kPa. Determine the temperature drop during this process and the final specific volume of the refrigerant.
A throttling valve is typically adiabatic and involves no work. Changes in kinetic and potential energies are negligible.
Under these conditions, a throttling process is isenthalpic, meaning the initial and final enthalpies are equal,
Identify the properties at initial and final states and then calculate the temperature drop and the specific volume (Table A-12).

## Slide 12: Tutorial Question Q10
Q10) Refrigerant-134a at 1 MPa and 90°C is to be cooled to 1 MPa and 30°C in a condenser by air. The air enters at 100 kPa and 27°C with a volume flow rate of 600 m /min and leaves 3 at 95 kPa and 60°C. Determine the mass flow rate of the refrigerant.
Energy balance on a steady-flow heat exchanger
Calculate the mass flow rate of air, using the properties of R-134a in Table A-12 and Table A-13
Calculate the mass flow rate of air, using Table A-17.
Calculate the heat transfer rate into air, i.e. the heat lost rate from R-134a
Find out the mass flow rate of R-134a.